## Slide 1
THESIS DEFENSE · 2026
IoT-Based Smart Home
System for Elderly Care
A full-stack platform combining ESP32 hardware, Clean Architecture backend, machine-learning anomaly detection, and a hybrid AI assistant.
STUDENT
Tu Dinh Huy
ID ITITIU21213
SUPERVISOR
Le Duy Tan, Ph.D.
International University — VNU-HCM
2026

## Slide 2
02
AGENDA
THESIS DEFENSE · ITITIU21213
2 / 20
Presentation Roadmap
01
Motivation & Problem
Aging Vietnam, gaps in commercial smart-home tech
02
Research Goals
Three research questions and implementation targets
03
System Architecture
4-layer IoT stack: hardware → cloud → backend → UI
04
Hardware Design
ESP32 node, sensor suite, custom 2-layer PCB
05
Backend
Flask + Clean Architecture, MQTT, REST + Socket.IO
06
Web & Mobile UI
Vite dashboard and Flutter app for caregivers
07
AI & ML Subsystem
Alfred + Isolation Forest, accuracy & inference latency
08
Validation & Security
April 2026 layer validation; auth, MQTT-TLS, rate limits
09
Limitations & Future
What's left, what comes next

## Slide 3
03
PART 1 — MOTIVATION
THESIS DEFENSE · ITITIU21213
3 / 20
Why an Open Smart-Home for Elderly Care?
BY 2050
~14%
of Vietnam's population
will be aged 65 or older
Source: GSO, 2019
THE PROBLEM
Coverage gaps in solo living
Elderly prefer home — but a fall, racing heart, or overheated room may go unnoticed between family visits.
Closed commercial ecosystems
Off-the-shelf smart-home products lock data in proprietary clouds with no anomaly alerting and no BLE health-sensor support.
No room-aware view for caregivers
Existing apps don't show where devices are within a floor plan, making spatial situational awareness hard.
MY GOAL: an affordable, open-source, full-stack platform for continuous elderly monitoring.

## Slide 4
04
PART 2 — RESEARCH GOALS
THESIS DEFENSE · ITITIU21213
4 / 20
Research Questions & Objectives
RQ 1
Sensing reliability
Can a low-cost IoT system reliably monitor environmental and physiological signals in a household?
RQ 2
ML on small data
Can a simple unsupervised ML model (Isolation Forest) provide useful anomaly detection on a small dataset?
RQ 3
Local LLM as UX
Can a locally hosted LLM serve as a practical interface for elderly users and caregivers?
IMPLEMENTATION GOALS
✓
ESP32 sensor node + custom PCB
✓
Flask backend (Clean Architecture)
✓
BLE heart-rate bridge
✓
Web dashboard + Flutter mobile app
✓
Alfred AI assistant (3 modes)
✓
Isolation Forest anomaly pipeline

## Slide 5
05
PART 3 — SYSTEM ARCHITECTURE
THESIS DEFENSE · ITITIU21213
5 / 20
Four-Layer IoT Stack
Hardware → Cloud broker → Backend → Web/Mobile UI
L1
Hardware
ESP32-WROOM-32 + DHT11, LDR, PIR, 2 relays. Telemetry every 5s over TLS-MQTT.
L2
Communication
EMQX Cloud MQTT broker (TLS port 8883). home/sensors/# and home/control/<code>.
L3
Backend
Flask + Clean Architecture. REST, Socket.IO, APScheduler, MQTT listener → ORM → MySQL.
L4
Presentation
Vite web SPA + Flutter mobile. Bearer-token auth, Socket.IO room isolation, real-time updates.
Figure 1 — System architecture (data + control flow)

## Slide 6
06
PART 4 — HARDWARE DESIGN
THESIS DEFENSE · ITITIU21213
6 / 20
ESP32 Node & Custom PCB
PCB 3D Render
Copper Layout (Altium)
Working prototype with LCD status
Coospo H6
BLE GATT 0x2A37
BPM bridge via Python (bleak)
240 MHz
Dual-core ESP32-WROOM-32 with hardware AES/TLS
5 sensors
DHT11 · LDR · PIR · Coospo H6 · 2 relays
16×2 LCD
I²C local status display (SDA 21 / SCL 22)
41 parts
Custom 2-layer PCB · 24 component types · Altium
Note: Wi-Fi and BLE cannot run concurrently on ESP32 → dedicated Python BLE bridge republishes BPM to MQTT.

## Slide 7
07
PART 5 — BACKEND
THESIS DEFENSE · ITITIU21213
7 / 20
Flask + Clean Architecture (5 Layers)
Presentation
Infrastructure
Gateways
Use Cases
Domain
Inward dependency rule: outer layers depend on inner abstractions.
Domain (innermost)
Device entities, abstract port interfaces. Zero framework imports — pure Python.
Use Cases
DeviceUseCase, AlertUseCase, SensorUseCase, AIUseCase, ReminderUseCase.
Gateways
MQTT listener/publisher, Socket.IO emitter, email notifier (SMTP / Brevo).
Infrastructure
SQLAlchemy ORM — 16 tables (users, devices, rooms, sensor_data, alerts, health, reminders).
Presentation
Flask blueprints — auth, device, room, alert, patient, reminder, ai, map, admin APIs.

## Slide 8
08
PART 5 — API SURFACE
THESIS DEFENSE · ITITIU21213
8 / 20
REST + Socket.IO + MQTT
30+ endpoints, real-time push, scheduled jobs, signed-token auth
REST API
30+
REST endpoints
› auth — login, register, password reset
› device — control, telemetry, history
› rooms / map — floors, polygons, devices
› patient — profile, HRV, health records
› alerts — list, ACK, delete, severity filter
› reminders — medicine schedules, dispatch
› ai — Alfred chat, mood, advice
› admin — caregiver CRUD, role gating
SOCKET.IO REAL-TIME
User-scoped event rooms — pushed only to the authenticated user.
device_status
ON/OFF state changes
sensor_update
5-second telemetry burst
alert
Anomaly / system alert
hr_alert
Heart-rate spike (Isolation Forest)
ai_mood
Alfred mood/persona update
ai_advice
Alfred contextual advice push
CROSS-CUTTING
Auth
Signed bearer tokens (itsdangerous, 7-day lifetime). @auth_required decorator.
Rate limits
500 req/day · login 10/min · register 5/min (Flask-Limiter).
Scheduler
APScheduler — automation rules, cron schedules, medicine reminders.
Docs
Swagger UI at /api/docs (OpenAPI 3.0).

## Slide 9
09
PART 6 — WEB DASHBOARD
THESIS DEFENSE · ITITIU21213
9 / 20
Vite + Vanilla JS Dashboard
Main Dashboard — bio-metrics, live BPM chart, alerts feed
Health
Alerts
Rooms
Command
🩺
Health Monitor
BPM time-series with risk colors. HRV — RMSSD, SDNN, pNN50.
🚨
Alert Management
Severity filters, per-alert ACK/delete, bulk-clear. CSV export.
🗺
Room Configuration
Polygon draw tool, floor tabs, drag-drop device assignment.
💡
Device Command
MQTT toggle controls, last-seen status, real-time state feedback.
👥
Care Staff (admin)
Caregiver CRUD, patient-caregiver linkage, role gating.

## Slide 10
10
PART 6 — MOBILE APP
THESIS DEFENSE · ITITIU21213
10 / 20
Flutter Cross-Platform App
Same auth flow and Socket.IO model as web — Android + iOS
Login & Auth
Device Control
Health Monitor
Alfred Chat
Voice input
speech_to_text — reduces typing for elderly
Map screen
Floor-plan polygons + device markers
3-mode AI
Rule / Ollama LLM / Gemini fallback
April 2026 ✓
Static analysis + tests + UI flows passed

## Slide 11
11
PART 7 — AI SUBSYSTEM
THESIS DEFENSE · ITITIU21213
11 / 20
Alfred — Hybrid AI Assistant
Three backend inference modes + a frontend overlay that compares them
RULE
< 50 ms
Rule mode
Pattern-matching engine for device toggles. Deterministic and offline-safe.
LLM (DEFAULT)
1 – 4 s
Ollama qwen2.5:3b
Local LLM with full context. No cloud, full privacy.
CLOUD
< 1 s
Gemini 2.5 Flash
Google Gemini for complex queries. Auto-fallback to Ollama on error.
OVERLAY
frontend
Compare mode
Calls all three sequentially, auto-selects the best reply.
CONTEXT-ENRICHED PROMPT
Live sensor state (T/H/L/PIR)
Device list & current ON/OFF
Patient profile (name, conditions)
Persona instruction
Recent conversation memory
Personalisation
Alfred addresses the user by their registered patient name. Voice input via Web Speech API and speech_to_text.

## Slide 12
12
PART 7 — ML ANOMALY DETECTION
THESIS DEFENSE · ITITIU21213
12 / 20
Isolation Forest on Heart-Rate Stream
PERFORMANCE ON 2,000-SAMPLE SYNTHETIC TEST SET
91%
RECALL
62%
PRECISION
4 RISK LEVELS
✓
Normal
△
Elevated
▲
High
!
Critical
ALERT PIPELINE
BLE Coospo H6
›
MQTT bridge
›
Isolation Forest
›
DB + Socket.IO
›
Web + Mobile
HRV Pipeline
RMSSD, SDNN, pNN50 computed from continuous BPM stream. Detects chronic autonomic deterioration over time.
Inference Cost
<1 ms per sample · O(T log n) · 300 trees. Not a runtime bottleneck — runs in real time on commodity hardware.
Training Data
2,000-sample synthetic held-out test set. Single feature: heart rate (BPM). scikit-learn implementation.

## Slide 13
13
PART 7 — ML METHODOLOGY
THESIS DEFENSE · ITITIU21213
13 / 20
How Precision & Recall Were Computed
From synthetic train/test split to confusion matrix to the headline metrics
Figure 2 — Training & evaluation pipeline (1700 train · 2000 test)
Training set
1,700 normal-only samples. Isolation Forest is unsupervised — anomalies aren't shown during training.
Test set
1,900 normal + 100 anomalous = 2,000 samples held out. Class imbalance ~5%.
Why these metrics
Accuracy is misleading at 5% imbalance. Recall captures missed anomalies; precision measures false-alarm rate.
RESULT ON 2,000-SAMPLE TEST
TP
91
anomaly → anomaly
FP
56
normal → anomaly
FN
9
anomaly → normal
TN
1,844
normal → normal
Precision = TP / (TP + FP) = 91 / 147 = 0.62
Recall = TP / (TP + FN) = 91 / 100 = 0.91

## Slide 14
14
PART 7 — ML INFERENCE LATENCY
THESIS DEFENSE · ITITIU21213
14 / 20
Measured Pipeline Latency
Real benchmark — perf_counter timer over N iterations · backend/tools/benchmark_latency.py
Figure 3 — Benchmark architecture (timer wraps production code)
MEASURED LATENCIES
T1
Rule check
~1 µs
if bpm ≥ 130 / ≤ 40
T2
HRV computation
0.13 ms
RMSSD · SDNN · pNN50
T3
ML inference
40.6 ms
scaler + anomaly + mood
T4
Total pipeline
40.8 ms
T1 + T2 + T3 end-to-end
Numpy-optimized path: T3 drops to 39.01 ms (–4 %)
1–4 s
Alfred LLM (Ollama qwen2.5:3b)
<50 ms
Alfred Rule mode (pattern match)
~17,000
DB rows/day per node (5 s bundle)

## Slide 15
15
PART 8 — VALIDATION
THESIS DEFENSE · ITITIU21213
15 / 20
Validation Results — April 2026
Every layer passed repository validation
Firmware
✓
Compiled & deployed to physical ESP32-WROOM-32
Both relays (light/fan) verified web + mobile
Sensor data confirmed in DB in real time
I²C LCD boot status, Wi-Fi/MQTT, relay state ✓
Backend
✓
pytest critical modules — PASS
Signed bearer-token auth — PASS
Rate-limit configuration — PASS
Ownership scoping (device/history) — PASS
Web
✓
Vite production build — PASS
Socket room-join + HRV endpoints — PASS
Alert ACK/delete + admin role gating — PASS
Map device-position stability — PASS
Mobile
✓
Static analysis (Flutter analyze) — PASS
Automated tests — PASS
Alfred patient-name greeting — PASS
Key UI flows + API integration — verified
Isolation Forest: 91% recall · 62% precision on 2,000-sample synthetic test set

## Slide 16
16
PART 8 — SECURITY
THESIS DEFENSE · ITITIU21213
16 / 20
Security Implementation
🔐
Authentication
Signed bearer tokens (itsdangerous, 7-day lifetime). @auth_required on all protected endpoints.
🔑
Password Storage
Werkzeug salted hashes. Plaintext never stored or logged anywhere.
⏱
Rate Limiting
Global 500/day, 100/hr. Login 10/min · 50/hr. Register 5/min.
🛡
SQL Injection
SQLAlchemy ORM with parameterised queries. No raw SQL string concatenation anywhere.
🔒
MQTT Security
EMQX TLS port 8883, per-topic ACL, credentials in local secrets header.
🌐
CORS
Explicit origins whitelist — all other origins return 403 on preflight.
KNOWN GAP: Flask API served over HTTP in thesis LAN. HTTPS via Nginx + Let's Encrypt is required before production deployment.

## Slide 17
17
PART 9 — LIMITATIONS
THESIS DEFENSE · ITITIU21213
17 / 20
Honest Limitations
What this thesis does and does not yet establish
01
Synthetic ML data only
Isolation Forest's 91%/62% recall/precision describes synthetic distribution. Not validated on real patient records.
02
No fall detection
MPU-6050 accelerometer integration is not in the current scope.
03
HTTP-only LAN prototype
Flask API served over HTTP — bearer tokens unprotected on untrusted networks. TLS hardening deferred.
04
Single-node testing
Only one ESP32 node tested — multi-room, multi-node scalability not measured.
05
No structured usability study
Formative observations only — no task-completion metrics or elderly participant sample.
06
Prototype-level auth flows
Account cancel and password reset are prototype-level. One-time tokens, session revocation, audit trails needed before deployment.

## Slide 18
18
PART 9 — FUTURE WORK
THESIS DEFENSE · ITITIU21213
18 / 20
Roadmap Beyond This Thesis
NEAR TERM
HTTPS production
Nginx + Let's Encrypt; Docker Compose already provided.
NEAR TERM
Fall detection
MPU-6050 accelerometer + Random Forest classifier.
MEDIUM TERM
Real patient data
Partner with geriatric clinic to retrain Isolation Forest.
NEAR TERM
Push notifications
Firebase Cloud Messaging for medicine reminders.
NEAR TERM
ESP32-side timing
Firmware-level timestamps for sensor → MQTT publish latency. Backend-side pipeline already measured.
MEDIUM TERM
Usability pilot
Task-completion rate with elderly users + caregivers.
LONG TERM
Multi-tenancy
Per-household data isolation, multi-resident caregiver dashboard.
LONG TERM
Camera occupancy
ESP32-CAM + TensorFlow Lite for person detection.
NEAR TERM
Auth hardening
One-time reset tokens, session revocation, audit trail.

## Slide 19
19
CONCLUSION
THESIS DEFENSE · ITITIU21213
19 / 20
What This Thesis Delivered
RQ 1 ✓
Sensing reliability
Low-cost IoT system (ESP32, MQTT, Flask) reliably monitors environmental and physiological signals — firmware and backend validated in lab.
RQ 2 ✓
ML on small data
Isolation Forest achieves 91% recall, 62% precision on synthetic test set. Clinical validation on real data is required before deployment.
RQ 3 ✓
Local LLM as UX
Alfred (Ollama qwen2.5:3b + Gemini fallback) provides a practical LLM interface. Voice input reduces barrier for elderly users.
FIVE TECHNICAL LAYERS DELIVERED
1
Hardware PCB (Altium, 41 parts)
2
Flask Clean Architecture backend
3
ML anomaly pipeline (Isolation Forest)
4
Vite web dashboard
5
Flutter mobile app
PRIMARY OUTSTANDING TASK
ESP32 firmware-side timing + real patient data collection — both required to move from validated prototype to clinically deployable system. Backend pipeline latency already benchmarked (T4 = 40.8 ms).

## Slide 20
Thank You.
QUESTIONS · DISCUSSION · FEEDBACK
Tu Dinh Huy · ITITIU21213
Supervisor: Le Duy Tan, Ph.D. · International University — VNU-HCM
2026